## Slide 1: Duck Workshop
UW Stout IEEE
Jack Hildebrandt

## Slide 2: 555 timers. How do they work
Three modes of operation:
  Astable mode – Works like a clock
  Monostable mode – Generates single pulses, PWM
  Bistable mode – Works similar to a flip-flop
Operate between 5 and 18 Volts
CMOS versions run at lower voltages >2v
This workshop uses a CMOS 555 timer (TLC555)

## Slide 3: The circuit: Astable Mode
ton ≈ 0.69*C1*(R1+R2)
toff ≈ 0.69*C1*R2
ton ≈ 1.5484 Sec
toff ≈ 0.7742 Sec

## Slide 4: Build a duck

## Slide 5: First components: LED and Capacitor
Flat part of LED matches with PCB
Negative stripe should be pointed to “C1” label as show

## Slide 6: Resistors
330 Ω blue resistor (R3) goes next to LED
5.1K Ω tan resistors (R1 & R2) go on the sides
  Tan resistors won’t quite fit. Angle them up (see example board)

## Slide 7: 555 timer
Bend pins in so they can fit in the holes
Make sure the circle shown in the photo matches your 555 timer. That’s a position indicator.

## Slide 8: Battery holder
Pop into two holes.
Make sure orientation matches picture

## Slide 9: Soldering
Solder from side shown
Snip excess wire

## Slide 10: Test
Insert battery.
Does it flash?

## Slide 11: Inserting into duck
Carefully cut a hole the approximate width and height of the circuit board.
Make sure LED and capacitor are in/around the duck’s head
Seal hole with electrical tape

## Slide 12: Decorate duck!